METES AND BOUNDS DESCRIPTION

0.0289 ACRE (1,261 SQUARE FEET)

E. B. COGSWELL SURVEY, ABSTRACT NUMBER 785

HARRIS COUNTY, TEXAS

Being an easement containing 0.0289 acre (1,261 square feet) of land situated in the E.B. Cogswell Survey, Abstract Number 785, Harris County, Texas; being out of and a portion of that certain called 1.245 acre tract conveyed to Kensinger Properties Limited (60%-Interest) by deeds recorded under Harris County Clerk’s File (H.C.C.F.) Numbers RP-2016-389828 and RP-2017-419245, and to Stuartfrank LLC (20%-Interest) by deed recorded under H.C.C.F. Number RP-2017-8046, and to KDCO Holdings LLC (20%-Interest) by deed recorded under H.C.C.F. Number RP-2018-550300, Harris County, Texas; and being out of and a portion of that certain called 0.1404 acre Sanitary Sewer Easement reserved to the City of Houston by instrument recorded in Volume 5558, Page 43 of the Harris County Deed Records, Harris County, Texas; said 0.0289 acre easement being more particularly described as follows (Bearings described herein are referenced to the Texas Coordinate System, South Central Zone No. 4204 (NAD83). All distances are surface and coordinates are grid and may be converted to surface values by applying the combined scale factor of 0.999870017):

COMMENCING for reference at a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” (X=3,086,233.049, Y=13,849,621.043) set marking the south end of a right-of-way (R.O.W.) cut-back line at the intersection of the west R.O.W. line of Antoine Road (Width Varies) as recorded under H.C.C.F. Number B340590 and Y580017 with the curved north R.O.W. line of Interstate Highway 10 (Also known As Katy Freeway) (Width Varies) and marking the most southerly southeast corner of said called 1.245 acre tract and marking the beginning of a curve to the right, from which a found Brass Disk stamped “TxDot” bears North 33°04’ East, 1.99 feet;

THENCE, Westerly, along said north R.O.W. line, an arc distance of 150.09 feet along said curve to the right, having a radius of 5,679.65 feet, a central angle of 01°30’51” and a chord which bears South 84°41’37” West, 150.09 feet to a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” set in the east line of Woodlawn Garden of Memories, a subdivision plat of record in Volume 28, Page 70 of the Harris County Map Records and marking the southwest corner of said called 1.245 acre tract;

THENCE, North 00°27’13” West, departing said north R.O.W. line and along the east line of said Woodlawn Garden of Memories and along the west line of said called 1.245 acre tract, a distance of 115.55 feet to a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” set marking the southwest corner of said called 0.1404 acre Sanitary Sewer Easement, from which a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” set marking the northwest corner of said called 1.245 acre tract bears North 00°27’13” West, 243.09 feet;

THENCE, North 88°36’16” East, along the south line of said called 0.1404 acre Sanitary Sewer Easement, a distance of 20.00 feet to a cut “X” in concrete set marking the southeast corner of said called 0.1404 acre Sanitary Sewer Easement;

THENCE, North 00°27’13” West, along the east line of said called 0.1404 acre Sanitary Sewer Easement, a distance of 94.56 feet to a point (X=3,086,101.958, Y=13,849,817.726) for an angle point in the east line of said called 0.1404 acre Sanitary Sewer Easement and for the southwest corner and POINT OF BEGINNING of the herein described easement;

METES AND BOUNDS DESCRIPTION

0.0289 ACRE

PAGE 2 OF 2

THENCE, North 00°27’13” West, crossing said called 0.1404 acre Sanitary Sewer Easement, a distance of 67.92 feet to a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” set marking an angle point in the east line of said called 0.1404 acre Sanitary Sewer Easement and marking the northwest corner of the herein described easement, from which a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” set marking the northeast corner of said called 0.1404 acre Sanitary Sewer Easement bears North 00°27’13” West, 80.54 feet;

THENCE, South 21°15’36” East, along the east line of said called 0.1404 acre Sanitary Sewer Easement, a distance of 40.33 feet to a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” set marking an angle point;

THENCE, North 88°38’58” East, continuing along the east line of said called 0.1404 acre Sanitary Sewer Easement, a distance of 18.67 feet to a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” set marking the northeast corner of the herein described easement;

THENCE, South 00°27’13” East, continuing along the east line of said called 0.1404 acre Sanitary Sewer Easement, a distance of 30.00 feet to a 5/8-inch iron rod with plastic cap stamped “Terra Surveying” set marking the southeast corner of the herein described easement;

THENCE, South 88°38’58” West, continuing along the east line of said called 0.1404 acre Sanitary Sewer Easement, a distance of 33.00 feet to the POINT OF BEGINNING and containing 0.0289 acre (1,261 square feet) of land.  This description is based on the Standard Land Survey and plat made by Terra Surveying Company, LLC. dated February 20, 2020, Project Number 1611-1601-S.

Compiled by: Robert J. Gabler, R.P.L.S.

Terra Surveying Company, LLC

3000 Wilcrest, Suite 210

Houston, Texas  77042

February 27, 2020

Project Number 1611-1601-S

1611-1601 KDCO San Sew Esmt MB 0.0289 Ac.doc